## Slide 1
NETWORK ENGINEERING PROJECT
Network Implementation
Final Report
Three-Tier Hierarchical Network Design & Deployment
7 Implementation Modules
Security Hardened
Fully Verified

## Slide 2
PROJECT OVERVIEW
Implementation Roadmap
01
Executive Summary
Project scope, objectives, and key achievements overview
02
Module 1: Infrastructure Foundations
Three-tier hierarchy, SSH, RSA keys, and device hardening
03
Module 2-3: VLANs & Trunking
VLAN segmentation, 802.1Q trunks, PortFast configuration
04
Module 4-5: LACP & L3 Routing
Link aggregation, Port-Channel, routed ports
05
Module 6: OSPF Dynamic Routing
OSPF configuration, adjacency, Router-ID management
06
Module 7: Security & NAT
PAT, ACLs, default routes, internet egress
Network Topology & Evidence
Complete topology diagram and verification screenshots
Key Learnings
Troubleshooting insights and lessons learned

## Slide 3
PROJECT OVERVIEW
Executive Summary
Project Objective
Design and deployment of a secure, redundant three-tier hierarchical network supporting enterprise-grade connectivity with segmented VLANs, high-speed backbone aggregation, dynamic routing, and secure internet egress.
Key Achievements
VLAN Segmentation
4 functional VLANs deployed
LACP Aggregation
Bundled Gigabit links
OSPF Routing
Dynamic routing enabled
NAT/PAT Security
Secure internet egress
Troubleshooting Journey
Each module presented unique challenges—from configuration mode errors and Spanning Tree delays to Port-Channel mismatches and OSPF adjacency failures. Every struggle led to deeper protocol understanding.
7
Implementation Modules
4
Functional VLANs
100%
Connectivity Verified
Real-world troubleshooting experience gained through hands-on problem resolution

## Slide 4
MODULE 01
Infrastructure Foundations & Hardening
Three-Tier Hierarchy
Used Auto-Connect tool to rapidly build the hierarchical structure, automatically linking Core, Distribution, and Access layers without manual port mapping.
Core Layer
Distribution
Access Layer
Security Implementation
SSH & RSA Keys
Secure remote access enabled
Privileged Passwords
Enable secret configured
Banner Message
Login warning activated
Verification
Enable Secret:
class
Console/VTY:
cisco
The Struggle: "Invalid Input" Errors
Problem:
Attempted to run crypto key generate rsa command but CLI kept rejecting with "invalid input" errors.
Root Cause Analysis
The command was being executed in privileged EXEC mode instead of global configuration mode. Additionally, device hostname and domain name must be set before generating RSA keys.
Resolution Steps
1.
Enter global config: conf t
2.
Set hostname: hostname Core-SW
3.
Set domain: ip domain-name network.local
4.
Generate keys: crypto key generate rsa
Lesson learned: Always verify configuration mode before executing global commands. The CLI context determines available command sets.

## Slide 5
MODULE 02-03
VLAN Segmentation & Trunking
VLAN Design
Divided the network into four functional VLANs to segment traffic and improve security and performance.
10
Management
Network devices
20
Finance
Financial systems
30
IT
Technical staff
99
Native
Trunk native VLAN
802.1Q Trunk Configuration
Configured trunks between all switches to allow VLAN traffic to travel across the network infrastructure.
switchport mode trunk
switchport trunk allowed vlan 10,20,30,99
Struggle #1: DHCP Failure
Symptom:
Host took too long to get an IP address on specific access port.
Diagnosis
Spanning Tree delay - Port was in learning/listening states before forwarding.
Solution
spanning-tree portfast
Allows immediate transition to forwarding state for host connectivity.
Struggle #2: Native VLAN Mismatch
Symptom:
Console flooded with Native VLAN mismatch error logs.
Solution
Manually synchronized VLAN 99 as native VLAN across all trunk links:
switchport trunk native vlan 99

## Slide 6
MODULE 04-05
Backbone Aggregation & L3 Routing
LACP Link Aggregation
Bundled Gigabit links using LACP (Link Aggregation Control Protocol) to increase backbone bandwidth and eliminate single points of failure.
Increased BW
Combined throughput
Redundancy
Failover protection
// Create Port-Channel interface
interface Port-channel1
switchport mode trunk
switchport trunk allowed vlan 10,20,30,99
Layer 3 Routing
Converted switch ports to Routed Ports for direct core router connection using Point-to-Point IP addressing.
// Convert to routed port
interface GigabitEthernet1/0/1
no switchport
ip address 10.0.0.1 255.255.255.252
no shutdown
Major Struggle: Port Suspension
Critical Problem
Switch suspended the ports due to configuration mismatches between physical interfaces and the virtual Port-Channel.
Root Cause
Physical interfaces had conflicting configurations (speed, duplex, trunk settings) that didn't match the Port-Channel interface parameters. LACP requires identical configurations on all bundled ports.
Resolution Strategy
1
Default the Ports
default interface gig1/0/1-2
2
Build from Port-Channel First
interface Port-channel1
Configure trunk settings here
3
Add Physical Interfaces
channel-group 1 mode active
Inherits settings from Port-Channel
This was the most difficult phase. The lesson: Always build Port-Channels from the virtual interface down, not from physical interfaces up.

## Slide 7
MODULE 06
Redundant Routed Backbone with OSPF
OSPF Configuration
Configured OSPF dynamic routing between Multilayer Switches and Core Routers to enable automatic route advertisement and failover.
// OSPF Configuration on Multilayer Switch
router ospf 1
router-id 1.1.1.1
network 192.168.10.0 0.0.0.255 area 0
network 192.168.20.0 0.0.0.255 area 0
network 192.168.30.0 0.0.0.255 area 0
network 10.0.0.0 0.0.0.3 area 0
Dynamic Updates
Auto route propagation
Load Balancing
Equal-cost paths
Verification Commands
show ip ospf neighbor
// Check adjacencies
show ip route ospf
// View OSPF routes
show ip protocols
// Verify OSPF status
OSPF Adjacency Failure
Problem
OSPF adjacency would not form between Core-R2 and multilayer switches. Neighbor table remained empty.
Dual Root Causes
Physical Port Mismatch
Cabling didn't match the configured interface assignments in the topology.
Missing Router-ID
Core-R2 had no explicit router-id, causing OSPF process instability.
Resolution
Corrected physical cabling to match topology documentation
Assigned explicit Router-ID on Core-R2:
router ospf 1
router-id 2.2.2.2
Result: Full end-to-end connectivity verified from all VLAN PCs through OSPF routing table.

## Slide 8
MODULE 07
Security, NAT & Internet Egress
PAT Configuration
Configured Port Address Translation (PAT) to allow multiple internal hosts to share a single public IP address for internet access.
// NAT Access List
access-list 1 permit 192.168.0.0 0.0.255.255
// PAT Configuration
ip nat inside source list 1 interface Gig0/0/0 overload
GUEST_RESTRICTION ACL
Implemented access control list to block internal network access while allowing verified internet traffic for guest VLAN.
// ACL Rules
deny ip 192.168.99.0 0.0.0.255 10.0.0.0 0.0.0.255
deny ip 192.168.99.0 0.0.0.255 172.16.20.0 0.0.0.255
permit ip any any
"Destination Host Unreachable"
Problem
Internet pings failed with "Destination host unreachable" errors. No external connectivity despite NAT configuration.
Root Causes Identified
Missing Default Route
No gateway of last resort configured on multilayer switches.
NAT Scope Too Small
ACL didn't include all 192.168.x.x VLAN ranges.
Resolution
1. Added Static Default Route:
ip route 0.0.0.0 0.0.0.0 10.0.0.6
2. Expanded NAT ACL:
access-list 1 permit 192.168.0.0 0.0.255.255
Final Status: All VLANs routing, Internet link active, GUEST_RESTRICTION confirmed on both multilayer switches with 151+ matches.

## Slide 9
REFLECTION
Key Learnings & Troubleshooting Insights
01
Configuration Mode Awareness
The Struggle
"Invalid input" errors when generating RSA keys
The Lesson
Always verify you're in global configuration mode (conf t) before executing global commands. CLI context determines available command sets.
02
Spanning Tree Behavior
The Struggle
DHCP failures due to port learning/listening delays
The Lesson
Apply PortFast on access ports connecting to end hosts. This bypasses STP learning states for immediate connectivity.
03
Port-Channel Build Sequence
The Struggle
Ports suspended due to configuration mismatches
The Lesson
Always build Port-Channels from the virtual interface down. Default physical ports first, then configure Port-Channel, then add members.
04
OSPF Router-ID & Physical Connectivity
The Struggle
OSPF adjacency wouldn't form
The Lesson
Verify physical cabling matches topology and always assign explicit Router-ID for OSPF stability.
05
NAT Scope Planning
The Struggle
"Destination host unreachable" errors
The Lesson
Ensure NAT ACL includes all internal subnets and always configure a default route for internet egress.
Overall Insight
Every struggle was an opportunity to understand the "why" behind the configuration. Troubleshooting not
only aided in fixing errors but also improved my
practical knowledge on the subject of networking

## Slide 10
Project Complete
All configurations saved to startup configuration
Network operational with full redundancy, security policies enforced, and internet connectivity verified
Fully Redundant
LACP + OSPF failover
Security Hardened
SSH, ACLs, VLAN segmentation
Internet Ready
NAT/PAT verified operational
Real-world troubleshooting experience gained through hands-on problem resolution